## Slide 1: Outline
Project and Task 1 Introduction
Data Review
Part Ranking
Dashboards
ER Diagram
Data Dictionary
Key Observations

## Slide 2: UofSC Roadmap

## Slide 3: Task 1: Exploration of Data
Understand headers
Get information on quality, ordering times, transportation, etc.
Identify poor areas/gaps in data
Make timeline of orders
Define states (early, tardy, too late)
Calculate numbers for tangible and intangible criteria ​
Create supplier ranking
Integrate findings into deliverable document ​
Deliverable: key figures from historical data,
rich/poor areas, supplier ranking

## Slide 4: Data Review: Reports
130 Reports
Summary
Focused on Material Master settings
Shows snapshot of plant at the time they are created
Includes vendor #, material #, and description
Key Fields
Rounding value
Safety time & stock
Days of supply
Net price

## Slide 5: Data Review: Reports
Zgrve Reports
Summary
Gives information on shipments once they arrive to the plant
Zgrve filed gives information on all the shipments for the day/date-range that it was created for
Key Fields
Material
Supplier #
Goods Receipts Date
Original & Current Goods Receipt/Diff. Qty

## Slide 6: Data Review: Reports
MD04 Reports
Summary
Shows information on demand forecast as well as real-time status on inventory and shipments
Shows demand, stock status, planned and past shipments (Sch. Agreements and Shipping Notifications)
Key Fields
Material
Demand Date
MRP Element
Change & Total Quantity
Line Index

## Slide 7: Data Review: User Documentation
Material Master Planner
Summary
Where all logistical data is stored and maintained
If not maintained, its impossible to create delivery schedules
Refer to when: There is unknown field or “view” information
Key Points
Relevant Views- MRP1, MRP2, and Classification
P-S Status
Lot Size
Procurement
Scheduling
Net Requirement Calculations

## Slide 8: Data Review: User Documentation
MC10/TS-12x
Summary
Shows the process for changing the forecasted requirements at the single item, single level
Summary of general information
Refer to when: needing general information about processes or exception messages
Key Points
Multiple Processes:
  Reschedule and Order Proposal
  Initial Pegged Requirements
General Info:
  Dependent and Independent Requirements
  Schedule Agreements
  Purchase Requisitions
  Planned Orders
  Scrap % Requirements

## Slide 9: Data Review: User Documentation
User Manual Bulk Planning Process
Summary
Daily Tasks of planners
Covers a lot of what has been seen in the interviews
Refer to when: There are questions about the planning process/refreshing on interviews
Key Points
Check A/B shift
Run Material Adjustment
Run MD07 SAP Transaction
Change Schedule per Exception Messages
Running MRP and Sending EDI Releases
Sending Zero Call Offs or Manually Creating Schedule Lines – AI Level Changes/Run Out Parts
Verifying XPLT Stock Movements

## Slide 10: Data Review: Interviews
The team met with 4 material planners to understand their thought process while planning, data used, and how they address problems.
Material Planners
Ben Shockley
Jeffrey Griggs
Tashelle Brady
Liliana Banda
Interview Objectives
Familiarize ourselves with the Planner’s daily tasks and the processes used to assess risk and make decisions regarding material planning forecasting.
Identify features that planners commonly use
Identify what capabilities would be helpful in a dashboard
Identify logic of current SAP system

## Slide 11: Part Ranking
A part ranking algorithm using Markov Chain is being developed
Based on historical data, we will be able to calculate the probability that an order will be early or late and by how many days for the next delivery.
Data Needed
Supplier number
Part number/description
Expected receipt date
Actual receipt date
Data Extracted From
Zgrve Reports
  Material (part #)
  Supplier #
  GR date (actual receipt date)
MD04 Reports
  Material
  Demand_Date/”ShipNt” in MRP Element

## Slide 12: Part Ranking: Data Usage
Part numbers are used to relate the information in the MD04 files and Zgrve reports
The expected date from MD04 is compared to the “goods receipt date” from Zgrve to obtain the difference in how many days late/early a part was delivered, and how often this happens (historical data)
This data is assumed to be a Markov chain and used to calculate long run probabilities of a supplier being early/late/on time and by how many days
Material # can be related to Supplier # to find out if a supplier is performing well or poorly across the board, or with specific parts

## Slide 13: Part Ranking: Example
For this specific sample part (bolded fields were created randomly) the data shows there is a 16% chance this part will arrive one day early, 33% chance it will arrive on time, 33% chance it will arrive one day late, and 16% chance it will arrive two days late (50% chance of late arrival)
The more historical data there is available, the more accurate the ranking is
Suppliers will be ranked based on % chance of on time arrival

## Slide 14: Part Ranking: Future Direction
Once underperforming parts have been identified, we can work on identifying the root cause
  Quality of supplied parts is not up to standards
  Supplier does not ship parts in time
  Transportation provider does not deliver parts in time
  Lead times are not calculated correctly
  Weather delays during a certain season
  Others
Identifying the cause for the delays and taking early action will help prevent them from happening in the future

## Slide 15: User Dashboards
The user dashboard will integrate all needed data and analysis into one location for the planner
The planner can view the status of their parts and a gauge will replace the stoplight to give a more exact representation.
The material planner suggestion will be displayed along with a box to collect the Planner’s feedback on why they accepted or rejected
The dashboard will also allow for creating “what if” scenarios based on alternative suppliers, transportation, stock, etc.

## Slide 16: Dashboards: Future Direction
Based on the observations from the interviews and continued understanding of planner’s needs, we would like to address the following in future development of the dashboards.
  Identify a way to streamline exception messages.
  There is an immense amount of “gut feeling” here, to address this, the front-end can be designed to maximize the quantification and qualification of machine learning on the back end.
  There seems to be an issue with standardization. We can tailor the front end to populate the backend, working to standardize it without interrupting user experience. A lot of this will come down to creating a system to allow for quick documentation of “gut feeling.”
  Asynchronous timers could be leveraged in a way they are not currently. It seems that some things are ‘put off until they can be dealt with’ and we can find better ways to manage these sorts of extraneous things

## Slide 17: Initial ER Diagram

## Slide 18
Material
Planner
has
Supplier
(Vendor)
1..*
supply
Material
(Part)
1..*
has
Material
Planning
Responsible
use
Material Inventory
use
Exception
generate
recommend
Health
Status
Output
input
input
0 %
100 %
Material Planner
Supplier
Material Config.
Material Trans.
Dashboard
Exception
Supply
Plant

## Slide 19: Data Dictionary for Material Planner
Objectives
  Identify most important columns for Material Planner
  Identify columns that can be imported from Parts DB
  Identify columns that can be generated by Reco. Engine and Forecast Model
Column | Possible Value
Name | 
Type | Text/Number/Date
Description | 
Source | Material Planner (or Part DB)/Algorithm
Frequency of change | High/Low/None
Purpose | Forecast Model, Reco. Dashboard, What..if
Data Dictionary Schema
Column | Possible Value
SafetyStck | 
Type | Number
Description | …
Source | Material Planner (or Part DB)
Frequency of change | Low
Purpose | Forecast Model, Reco. Dashboard, What..if
Example

## Slide 20
Material Planner
MRPCn (PK)
Planner Name
Vendor ID (FK)
Supplier
Vendor ID (PK)
Vendor Name
Material ID (FK)
Material Config.
Material ID (PK)
Material Desc
Safety Stock (number, Qty)
Planning Time Fence
Safety Time
Planning Calendar
Exception
Exception ID (PK)
Exception Msg
Dashboard
Material ID (FK)
Health Status (number , 0-100 in %)
Stock DoS (number, in Days)
First Receipt DoS (number, in Days)
Exception ID (FK)
?
?
Plant
Plant ID (PK)
Plant Location
MRP Area
Material Transaction
Material ID (FK)
Plant ID (FK)
MRPCn (FK)
Vendor ID (FK)
Shipment ID (FK)
Demand Date (Date, TimeStamp)
MRP Element (Text, category)
Change Qty (number, Qty)
Total Qty (number, Qty)
Supply
Shipment ID (PK)
Material ID (FK)
Vendor ID (FK)
Purchase Order #
Trailer ID (number, Key)
Source of Shipment (Lat., Lng, Address)
Dest. of Shipment (Lat., Lng, Address)
ETA to Dest. (number, hrs.)
Supply TS (Date, TimeStamp)
Material Planner
KPI

## Slide 21: MRP Element Possible Values
MRP Element | Description
Stock | An Initial stock value
DepReq | It specifies requirement/demand/consumption of a part.
ShipNt | Number of stck in transit; The trailer which is carrying the parts is in transit. It is expected to be at the delivery location on a demand date.
SchAgr | The quantity of stck we are expecting to collect from a supplier. It will be delivered on a demand date.
IndReq | Order Forecast of stock
SafeSt | It specifies the quantity whose purpose is to satisfy unexpectedly high demand in coverage period. The risk of shortfalls is reduced by having a safety stock.

## Slide 22: Key Observations

## Slide 23: Supporting Material

## Slide 24: Interview Summary: Jeffrey Griggs 9 years at BMW, 20 years in Automotive Industry
Few EO’s -> Logical Planner
Doesn’t look at traffic lights/exception messages- looks at lowest coverage days and MRP/Inventory discrepancies first
Running behind schedule- notifies to push parts out
  Ignore, unless weather, known line-shutdown, or Alfred says to not ignore
Rounding value- layer quantity on a palette, minimum order quantity (ASN Project?)
  Dependent Vs Independent Requirements
  Dependent -actual orders
Independent- more of a forecast, numbers appear more stable in SAP as a result
Semi Conductor Parts- changes very frequently due to availability of parts
  Production runs ahead during the week and stops early Saturday
Time Fence
  No hard answer for calculating, varies by planner
  Keep close as possible to pickup days, too far out can lead to running out of parts
  Planned delivery Time < Actual Coverage < Lead Time from Supplier

## Slide 25: Interview Summary: Tashelle Brady 25 years experience
Planner for local suppliers and suppliers from Mexico, local can do same day delivery
Overall Approach- Let the system plan, then evaluate exceptions
  Is it reasonable? Will it disrupt anything else? (Especially when stock is low).
Looks at exception messages first
Organize MRP numbers by vendor, haul, and source (bulk, JIT, etc)
Re-runs MRP to accept changes and check for gaps of “high-runners”
Exception messages in Time Fence: Ignored. Exceptions outside the Time Fence: let MRP system replan
Inputs safety stock when:
  It’s cheaper than expediting in future
  Doesn’t take up much space
  Is high-quality
Almost never pushes supply, except for:
  Short-term emergency
  Level-loading
What would be helpful:
  Automatic run of MRP after 2am, before any planning the next day
  No one day pickups for suppliers in Mexico -> split into two to prevent EO or loss

## Slide 26: Interview Summary: Liliana Banda ~3 years at BMW Material Planning
Planner for parts from Mexico
PTA is for rescheduling lines, EO is for extra inventory/new lines
Safety Stock:
  For “low runners”
Material Planner sets safety lead time

## Slide 27: Interview Summary: Ben Shockley 4 years as Material Planner, 19 years at BMW

## Slide 28: Part Ranking: Improvements
This will allow to calculate the monetary value a supplier represents
The lower the long run cost, the better the supplier is performing

## Slide 29
Material Planner
MRPCn (PK)
Planner Name
Vendor ID (FK)
Supplier
Vendor ID (PK)
Vendor Name
Material ID (FK)
Material Config.
Material ID (PK)
Material Desc
Safety Stock (number, Qty)
Planning Time Fence
Safety Time
Planning Calendar
Exception
Exception ID (PK)
Exception Msg
Dashboard
Material ID (FK)
Health Status (number , 0-100 in %)
Stock DoS (number, in Days)
First Receipt DoS (number, in Days)
Exception ID (FK)
?
?
Plant
Plant ID (PK)
Plant Location
MRP Area
Material Transaction
Material ID (FK)
Plant ID (FK)
MRPCn (FK)
Vendor ID (FK)
Shipment ID (FK)
Demand Date (Date, TimeStamp)
MRP Element (Text, category)
Change Qty (number, Qty)
Total Qty (number, Qty)
Supply
Shipment ID (PK)
Material ID (FK)
Vendor ID (FK)
Purchase Order #
Trailer ID (number, Key)
Source of Shipment (Lat., Lng, Address)
Dest. of Shipment (Lat., Lng, Address)
ETA to Dest. (number, hrs.)
Supply TS (Date, TimeStamp)
Material Planner
KPI

## Slide 30
Material Planner
MRPCn (PK)
Planner Name
Vendor ID (FK)
Supplier
Vendor ID (PK)
Vendor Name
Material ID (FK)
Material Config.
Material ID (PK)
Material Desc
Safety Stock (number, Qty)
Planning Time Fence
Safety Time
Planning Calendar
Exception
Exception ID (PK)
Exception Msg
Dashboard
Material ID (FK)
Health Status (number , 0-100 in %)
Stock DoS (number, in Days)
First Receipt DoS (number, in Days)
Exception ID (FK)
?
?
Plant
Plant ID (PK)
Plant Location
MRP Area
Material Transaction
Material ID (FK)
Plant ID (FK)
MRPCn (FK)
Vendor ID (FK)
Shipment ID (FK)
Demand Date (Date, TimeStamp)
MRP Element (Text, category)
Change Qty (number, Qty)
Total Qty (number, Qty)
Supply
Shipment ID (PK)
Material ID (FK)
Vendor ID (FK)
Purchase Order #
Trailer ID (number, Key)
Source of Shipment (Lat., Lng, Address)
Dest. of Shipment (Lat., Lng, Address)
ETA to Dest. (number, hrs.)
Supply TS (Date, TimeStamp)
Material Planner
KPI

## Slide 31
Material Planner
MRPCn (PK)
Planner Name
Vendor ID (FK)
Supplier
Vendor ID (PK)
Vendor Name
Material ID (FK)
Material Config.
Material ID (PK)
Material Desc
Safety Stock (number, Qty)
Planning Time Fence
Safety Time
Planning Calendar
Exception
Exception ID (PK)
Exception Msg
Dashboard
Material ID (FK)
Health Status (number , 0-100 in %)
Stock DoS (number, in Days)
First Receipt DoS (number, in Days)
Exception ID (FK)
?
?
Plant
Plant ID (PK)
Plant Location
MRP Area
Material Transaction
Material ID (FK)
Plant ID (FK)
MRPCn (FK)
Vendor ID (FK)
Shipment ID (FK)
Demand Date (Date, TimeStamp)
MRP Element (Text, category)
Change Qty (number, Qty)
Total Qty (number, Qty)
Supply
Shipment ID (PK)
Material ID (FK)
Vendor ID (FK)
Purchase Order #
Trailer ID (number, Key)
Source of Shipment (Lat., Lng, Address)
Dest. of Shipment (Lat., Lng, Address)
ETA to Dest. (number, hrs.)
Supply TS (Date, TimeStamp)
Material Planner
KPI